## Slide 2
Side view
Top view

## Slide 3
To take a compass reading
the compass must be level
Level the compass with the
Bubble level. When its level
The bubble is in the middle

## Slide 4
Bad
Bad
Good!

## Slide 5
It can be hard to get the bubble in the center and
the compass pointing at your target.

## Slide 6
The north arrow always
aligns to magnetic fields.
Some compasses have it as
A white tip ( no N )

## Slide 7
To read the compass, write down
what number the N points to

## Slide 8
What compass reading is this?
Also notice how the compass is
backwards? Any ideas why?

## Slide 9
The reversed compass is so that
you can just read what is written.
When you are “looking” East
The arrow will be on the East side.

## Slide 10: What this looks like in your notebook
Reading 1: 115° Volcano Peak from Hotel Balcony

## Slide 12
Dip and dip direction:
Find the lever on the back of
the compass.
While looking at the compass
face, move the lever around

## Slide 13
The Dip is the angle something
is going into (or out of) the Earth
What would this dip reading be?

## Slide 14
The bubble in the long tube
Is our guide to knowing if the
Compass is level.
Only take a reading
when its in the middle

## Slide 15
We also want to know which way
the rock is dipping. This is called
Dip Direction
Line up the back mirror side to be
parallel to the rock

## Slide 16
Keep the whole back edge of the
Compass on the rock.
Remember for a compass reading
to keep the compass level with the
circular level

## Slide 17
Some people like to use
their field note book to help

## Slide 18: What this looks like in your notebook
Reading 37: On the red sandstone bed at the parking lot I measured a Dip of 25° dipping towards 257°